Elmeg Phone Setup

Login

‘Display Name’ is the name of the user. ‘Account’, and ‘Authentication Username’ should be set to the extension number of the phone, and ‘Registrar’ is the IP address provided with the Orbtalk Welcome letter.

SIP

‘Outbound Proxy’ must be set to the same IP address as ‘Registrar’ was set to. Also make sure that ‘Long SIP-Contact’ is set to “off”, and that ‘Support broken Registrar’ is “on”.

NAT

‘Offer ICE’ should be “off”, and ‘Symmetrical RTP’ should be set as “on”. A ‘Keepalive interval’ of around “3” seconds is recommended.

Advanced Settings

Check that ‘Challenge Response on Phone’ is set to “off”, and ‘Filter Packets From Registrar’ is set to “off”.