Linksys SPA models

Factory Reset

Using the phone menu, select option (paper corner turned over icon) 14.

Obtain IP Address

Using the phone menu, select option (paper corner turned over icon) 9.

Firmware

For latest firmware download view the following link ;

http://www.linksys.com/servlet/Satellite?c=L_CASupport_C2&childpagename=US%2FLayout&cid=1169671627625&pagename=Linksys%2FCommon%2FVisitorWrapper&lid=2762542850B13&displaypage=nodata#versiondetail

User

Navigate to ‘Admin Login’, then ‘Advanced’.

Under ‘User’, the ‘CW Setting’ must be set to “no” (as highlighted below).

Ext 1

Proxy and Registration

‘Proxy’ and ‘Outbound Proxy’ are both set to the IP address provided with the Orbtalk Welcome Letter, and ‘Use Outbound Proxy’ must be set to “yes”.

Subscriber Information

‘Display Name’ is the name of the user. ‘User ID’, and ‘Auth ID’ should be set to the extension number of the phone.

Dial Plan

In the ‘Dial Plan’ dialogue, an additional “x” needs to be present (as highlighted below).

Set Voicemail

Using the phone menu, select option (paper corner turned over icon) 8. Enter *123 as the “VoiceMailNumber”.